## Slide 1: Automatic Calibration of Camera and Range Sensors Using Polygonal Planar Boards
Thai K. Nguyen, Xuan Truong Nguyen, Hyuk-Jae Lee
Seoul National University, CAPP Lab
2017.11.24

## Slide 2: Content
Introduction
Previous Research
Proposed Approach
Evaluation
Conclusion
References

## Slide 3: Introduction
Our setup of LiDAR and Camera
LiDAR (Light Detection And Ranging) has ben widely used in Advanced driver-assistance systems
  Has advantages due to its accuracy
It is usually used along with cameras
  Has advantages of their resolution
To fuse data from these sensors, calibration is required
  Here, we focus on calibration between a LiDAR and a Camera
  Specifies how to convert measurements from a LiDAR to the image coordinate
LIDAR
Camera

## Slide 4: Introduction
Front image
Calibration problem
  Inputs: Lidar scan{(xn, yn, zn)} and image {(um, vm)}
  Output: Calibration matrix M
  Method: With matching points, it can be solved using:
How to find matching points between 2 system coordinates
How to handle errors?
x
y
z
Only front view
LiDAR scan

## Slide 5: Previous Research
Many calibration algorithms use checkerboards as target
  However, they are often observed with range discrepancies
Checkerboard (a), monochromatic board (c) and their measurements on LiDAR

## Slide 6: Previous Research
Some methods using monochromatic board are proposed
  In [3], Park uses a monochromatic polygonal board
  Estimates its edges and intersects them to find the vertices
  However, with the monochromatic board, the process is more challenging to automate
    This paper still requires manual interventions
Triangle monochromatic board, estimated edges and vertices
Y. Park et al., “Calibration between Color Camera and 3D LIDAR Instruments with a Polygonal Planar Board”, Journal of Sensors, Vol. 14 no. 3, 2014.

## Slide 7: Proposed Approach
Method: Adopt background subtraction method for automating
Take two samples with and without the board
Subtract on both 2D image and 3D Lidar data
Board area is the largest segment of the subtraction output
Frame 2.5D data
Background 2.5D data
Background Subtraction
Board Segmentation
Corner Detection
Images
Background Subtraction
Matrix Estimation
Refinement
Corner Detection

## Slide 8: Proposed Approach
Board corners detection on the images
  Input and background image are subtracted
  Corners are calculated by intersecting estimated edges
image
background
subtraction
board segment
edge and corner estimation result

## Slide 9: Proposed Approach
Board corners detection on LiDAR data
  Background subtraction on 2.5D images are performed as above
  Board area is then expanded to full segment in 3D space
  Board border points are detected to estimate its edges
  Corner is estimated by intersecting edges
v1
v2
v1
outliers
Board segment
Border points
Estimated edges and corners

## Slide 10: Proposed Approach
Result
Occlusion. 3D points of the wall
Occluded area
Camera-LiDAR Fusion Results

## Slide 11: Proposed Approach
Result
  Estimated compared between multiple evaluations
  Differences is small. The Estimation M is robust
-0.25537 | -0.66648 | -0.07779 | 0.207338
0.182066 | -0.28306 | 0.559492 | -0.12347
0.00073 | -0.00095 | -0.00012 | -9.10E-05
-0.25841 | -0.66448 | -0.07331 | 0.197904
0.181116 | -0.2858 | 0.564159 | -0.11992
0.000729 | -0.00096 | -9.76E-05 | -6.46E-05
-0.25755 | -0.66597 | -0.07707 | 0.201721
0.181622 | -0.28465 | 0.560895 | -0.1221
0.00073 | -0.00095 | -0.00011 | -7.83E-05
Calibration matrix over 3 evaluation of same data
Evaluation 1
Evaluation 2
Evaluation 3
-0.25537 | -0.66648 | -0.07779 | 0.207338
0.182066 | -0.28306 | 0.559492 | -0.12347
0.00073 | -0.00095 | -0.00012 | -9.10E-05
-0.26139 | -0.66142 | -0.08091 | 0.182558
0.185615 | -0.29203 | 0.568633 | -0.10601
0.000727 | -0.00094 | -0.00011 | -0.00014
-0.25358 | -0.66517 | -0.07531 | 0.209922
0.182305 | -0.28996 | 0.561667 | -0.10351
0.000729 | -0.00096 | -0.00011 | -4.65E-05
Calibration matrix over 3 different data
data 1
data 2
data 3

## Slide 12: Evaluation
12 positions of the board => 48 correspondences
Use k positions to calculate matrix (k=3,4,5…)
Project all 3D vertex to its images
Calculate distance from projected point to ground truth
  Obtain the mean projection errors
Chart: Mean Projection Error (pixel)
Mean Projection Error | 3.3855 | 2.7739 | 2.2082 | 1.9763
Number of positions
2
3
4
5
 | Estimated (m) |  | Ground truth (m)
 | Mean | std | 
Width | 0.656575 | 0.017681 | 0.609
Height | 0.980834 | 0.016232 | 0.906
Estimation width and height of the board

## Slide 13: Conclusion
By using background subtraction the calibration process is automated in our implementation
  No manual intervention required
The final result is robust
  Robust for low-resolution
  Mean projection error reaches under 2pixel

## Slide 14: References
[1] Nguyen Van Thang, Hyuk-Jae Lee, "Car detection with a cascad-ed HOG classifier and a deformable part model," International Conf-erence on Green and Human Information Technology 2015, Feb. 2015.
[2] Xuan Truong Nguyen, Dinh Van Luan, Hyun Kim, Hyuk-Jae Lee, "A High-Definition LIDAR System Based on Two-Mirror Deflection Scanners," IEEE Sensors Journal, 2017.
[3] Park Y, Yun S, Won CS, Cho K, Um K and Sim S, "Calibration between color camera and 3D LIDAR instruments with a polygonal planar board", Sensors (Basel) , 2014.
[4] H. Alismail, L. D. Baker and B. Browning, "Automatic Calibration of a Range Sensor and Camera System," 2012 Second International Conference on 3D Imaging, Modeling, Processing, Visualization & Transmission, Zurich, 2012.