## Slide 1: ROI-based LiDAR sampling in the road environment
Nguyen Khac Thai
2018.05.25

## Slide 2: Content
Introduction
Previous approaches
Proposed algorithm
Experiment results
Conclusion

## Slide 3: Introduction
LiDAR sampling rate is low
  Lead to the problem of sampling to increase the efficiency
  Our lab’s lidar system [1]
    Be able to measure any desired locations in any order
    Sampling rate is limited to 100,000 measurements per second
The sampling problem
  Find a sampling map specifies which points should be sampled
[1] Xuan Truong Nguyen, Dinh Van Luan, Hyun Kim, and Hyuk-Jae Lee, "A High-Definition LIDAR System Based on Two-Mirror Deflection Scanners," IEEE Sensors Journal, Volume: 18, Issue: 2, Pages : 559-568, Jan. 2018.
Uniform or grid sampling; the most common sampling strategy

## Slide 4: Previous approaches
Depth-gradient-based sampling [2]
  Propose that sampling along the depth gradient gives the optimal result
    Successfully recover the depth map in Middlebury dataset with 5% of samples
  Inspired for compress sensing
    In real systems, depth gradient is not available before sampling
Two-step sampling [3]
  Apply depth-gradient-based sampling in a practical manner
    Step 1: Sample uniformly with half budget and reconstruct to find the gradient of reconstructed map
    Step 2: Sampling along the gradient map
  Not effective for complex scenes with a significant amount of outliers
[2] S. Hawe, M. Kleinsteuber, and K. Diepold, “Dense disparity maps from sparse disparity measurements,” in Proc. IEEE Int. Conf. Computer Vision (ICCV’11), Nov. 2011, pp. 2126–2133.
[3] L.-K Liu, S.H. Chan, and T.Q. Nguyen, “Depth reconstruction from sparse samples: Representation, algorithm, and sampling,” IEEE Trans. on Image Process., vol. 24, no. 6, pp. 1983–1996, Jun. 2015.
Gradient-based sampling (a) compared to grid sampling (b) and random sampling (c)

## Slide 5: Proposed approach
Our application of LiDAR sampling with ADAS
  Objective
    Gather more information ROI area, especially the objects area
      The design covers the case of a very low sampling rate (roughly 1%)
  Region of Interest (ROI) includes
    The road
    The objects
      Cars that are on the road
      Cyclists and pedestrians
Road
Cars, cyclists, pedestrians
A typical road scene in KITTI dataset

## Slide 6: Proposed approach
Workflow
  Capturing an image by the camera
  Image segmentation to 3 areas: road, objects, and background
  Sampling process (the focus of this work)
Proposed approach
  Move a portion of samples outside ROI into ROI area
    In existing systems, the sampling rate is equal in entire Field of View
  Inside ROI, move samples from the road to objects area
    In existing systems, road area has 6.75 times more samples than objects area
Segmentation
Road detection
Object detection
Image
Sampling
Background
ROI
Road
Objects

## Slide 7: Proposed approach
Budget distribution between ROI and non-ROI
  Increase sampling rate inside ROI while keeping localization result
    Given total budget N, the budget for ROI NROI and non-ROI NnROI are determined as:
      NROI + NnROI = N
      NROI =
      With
        and are the area of ROI and non-ROI
        and are regulation parameters (= 1.5, = 0.65)
          The increase ofindicates that more samples are moved from non-ROI to ROI area
          indicates the minimum of sampling budget must be kept inside non-ROI area to preserve the localization result
      If / is small, the first term is chosen
      If / is large, the second term is chosen
        Reserve a sampling rate outside ROI enough to keep the localization result
        Localization process determines the movement of the sensor and the car

## Slide 8: Proposed approach
Budget distribution inside ROI
  Characteristics of reconstruction quality in road and objects area
    Mean Absolute Error (MAE) of the road area converges very fast, starting from 0.11%
      This convergence is stable in all tested images
    MAE of objects area is much worse and no convergence found
      Indicate the need to increase the rate in objects area as high as possible
(a) Road area
Reconstruction result of the road and objects’ area in dependency of sampling rate
(b) Objects’ area
Chart: Sampling rate (%)
| 1.8050541516245487E-2 | 3.6101083032490974E-2 | 7.2202166064981949E-2 | 0.10830324909747292 | 0.1444043321299639 | 0.18050541516245489 | 0.21660649819494585 | 0.25270758122743681 | 0.28880866425992779 | 0.36101083032490977 | 0.57761732851985559 | 0.72202166064981954 | 0.86642599277978338 | 1.0830324909747293 | 1.4440433212996391 | 1.8050541516245489 | 2.1660649819494586 | 3.6101083032490977 | 7.2202166064981954
AVG | 5.7075 | 3.5214 | 0.42855 | 0.21975 | 0.19558 | 0.18548 | 0.18297 | 0.17882 | 0.17734 | 0.17668 | 0.17173 | 0.17009 | 0.16918 | 0.16802 | 0.16751 | 0.16642 | 0.16682 | 0.16601 | 0.1676
AVG-STD | 2.9108 | 2.1236 | 0.18405 | 0.14174 | 0.11934 | 0.10844 | 0.10607 | 0.10195 | 0.10273 | 0.097253 | 0.090308 | 0.089622 | 0.088357 | 0.089138 | 0.087071 | 0.086282 | 0.087121 | 0.086128 | 0.086861
AVG+STD | 8.5043 | 4.9192 | 0.67304 | 0.29775 | 0.27181 | 0.26252 | 0.25987 | 0.25569 | 0.25195 | 0.2561 | 0.25315 | 0.25055 | 0.25 | 0.24691 | 0.24796 | 0.24655 | 0.24652 | 0.24589 | 0.24834
Chart: Sampling rate
| 1.4440433212996391 | 2.1660649819494586 | 2.8880866425992782 | 3.6101083032490977 | 4.3321299638989172 | 5.0541516245487363 | 5.7761732851985563 | 6.4981949458483754 | 7.2202166064981954
AVG | 3.2651 | 2.7743 | 2.5077 | 2.4222 | 2.3085 | 2.2409 | 2.1841 | 2.1331 | 2.099
AVG-STD | 1.3125 | 1.1304 | 1.0918 | 0.99785 | 0.92863 | 0.87952 | 0.82279 | 0.78828 | 0.75474
AVG+STD | 5.2178 | 4.4181 | 3.9237 | 3.8465 | 3.6884 | 3.6023 | 3.5454 | 3.478 | 3.4432

## Slide 9: Proposed approach
Budget distribution inside ROI
  The MAE results of road and objects area are modeled in order to predict the overall results
    Above MAE results of road and objects area are well modeled to a rational function
      F(x) =
      For road: a = 0.1627; b = 0.00739; c = 0.02555;
      For object: a = 1.831; b = 2.011; c = 0.03956;
Original vs modeled function

## Slide 10: Proposed approach
Budget distribution inside ROI
    Given budget N, the area of road Sr and object So, The budget for road area Nr and objects area No is found by optimizing:
      Nr + No = N
      Minimize
        F1 and F2 are the modeled function for road and objects area as above
        is the weighting parameter between road and objects area
          =1 the criteria becomes predicted MAE of ROI area
          increases, the budget for objects area increases
      Budget distribution on the dependence of
        Sampling budget for objects area increase as increases, leads to the decrease in MAE results
 | Budget (%) |  | MAE (m) |  | 
 | for road | for objects | objects | road | ROI
1 | 55.8 | 44.2 | 2.232 | 0.1802 | 0.2583
1.4 | 53.1 | 46.9 | 2.207 | 0.1848 | 0.2635
2 | 50.2 | 49.8 | 2.183 | 0.1862 | 0.2645
 | Budget (%) |  | MAE (m) |  | 
 | for road | for objects | objects | road | ROI
1 | 55.8 | 44.2 | 2.232 | 0.1802 | 0.2583
1.4 | 53.1 | 46.9 | 2.207 | 0.1848 | 0.2635
2 | 50.2 | 49.8 | 2.183 | 0.1862 | 0.2645

## Slide 11: Experiment result 1 (Inside ROI)
Environment Setup
  KITTI dataset is used for experiments
    The raw depth as input and ground truth for evaluation
    Inside ROI, raw depth has a sampling rate of 7-8%
  Budget inside ROI is fixed with 1000 samples/scan
    Approximately 1% sampling rate
  Methods in evaluation
    (1) Random sampling
    (2) Two-step sampling
    (3) Proposed algorithm
Raw scan
Ground truth
An example of KITTI raw and ground truth depth image

## Slide 12: Experiment result 1 (Inside ROI)
Objective evaluation
  Sampling mask
    The proposed sampling algorithm has much denser mask in the objects’ area
(a) Full mask of raw depth
(b) Random sampling
(c) two-step sampling
(d) Proposed algorithm
Full set of available samples on raw depth (a) and sampling mask of random sampling (b), two-step sampling (c) and proposed algorithm (d)

## Slide 13: Experiment result 1 (Inside ROI)
Objective evaluation
  Reconstruction result
    The proposed algorithm has denser sampling rate in objects’ area
    Consequently, it produces better reconstruction result
(a) Ground truth
(d) two-step sampling
(e) Proposed algorithm
(c) Random sampling
(b) From raw depth (upper-bound performance)
Zoomed out of objects’ area in depth ground truth (a) and the reconstruction result from raw depth (b), random sampling (c), two-step sampling (d) and proposed algorithm (e)

## Slide 14: Experiment result 1 (Inside ROI)
Quantitative evaluation
  The sampling budget is N = 1000 samples/scan
  Comments
    With the same sampling budget, the proposed algorithm gives the best result in objects area
      Objects area is the main Region of Interest
    With little scarifying on road area (2cm in MAE), the proposed method yields the best overall result
N | Method | MAE (m) |  | 
 |  | Object | Road | ROI
1000 | Random | 3.453 | 0.1699 | 0.3037
 | Two-step | 2.946 | 0.1653 | 0.2799
 | Proposed | 2.207 | 0.1848 | 0.2635

## Slide 15: Experiment result 2 (entire FOV)
Environment setup
  Budget for entire Field Of View is fixed with 2000 samples/scan
    Approximately 1% sampling rate
Sampling mask comparison
Image of the scene

## Slide 16: Experiment result 2 (entire FOV)
Environment setup
  Budget for entire Field Of View is fixed with 2000 samples/scan
    Approximately 1% sampling rate
Sampling mask comparison
Sampling mask of random sampling

## Slide 17: Experiment result 2 (entire FOV)
Environment setup
  Budget for entire Field Of View is fixed with 2000 samples/scan
    Approximately 1% sampling rate
Sampling mask comparison
Sampling mask of two-step sampling

## Slide 18: Experiment result 2 (entire FOV)
Environment setup
  Budget for entire Field Of View is fixed with 2000 samples/scan
    Approximately 1% sampling rate
Sampling mask comparison
  The proposed algorithm has more sample in objects area
Sampling mask of proposed algorithm

## Slide 19: Experiment result 2 (entire FOV)
Quantitative results
  Comments
    Proposed algorithm concentrates samples to objects area with little sacrifice of localization result
    The reconstruction results of ROI area, especially the objects area are significantly improved
      MAE of objects area with the proposed approach reduces 49.1% compared to that with random sampling
Budget | Method | MAE (m) |  |  |  | Localization - translation drift(m)
 |  | objects | road | ROI | background | 
2000 | Random | 2.2953 | 0.143 | 0.3771 | 0.9699 | 0.12461
 | Two-step | 2.1221 | 0.141 | 0.3819 | 0.9128 | 0.09205
 | Proposed | 1.1684 | 0.1972 | 0.3241 | 1.048 | 0.12103

## Slide 20: Conclusion
This thesis proposes an algorithm to distribute LiDAR sampling budget in the road environment
  A portion of the budget for non-ROI area is moved to ROI area with the consideration of preserving the localization results
  A portion of the budget for road area is moved to objects area, which simultaneously increases reconstruction result of entire ROI
  Final MAE of objects area reduces 49.1% compared to random sampling and 44.9% compared to two-step sampling
Future work
  Synchronization between image and sampling process is an open issue to be solved in the future

## Slide 21: Appendix
Observation 1
  If a number of samples is moved from non-ROI area to ROI area, the localization results remain stable
    The localization is archived by Iterative Closest Points (ICP)
      The accuracy of ground truth is 0.1m translation drift (from KITTI)
      If we move out 20% of samples from non-ROI to ROI area, the result stays close to the ground truth accuracy
      When no sampling in non-ROI area ( = 100%), there is a huge decrease in localization accuracy
N | Method | translation drift (m) | rotation drift (degree)
2000 | = 0% | 0.1096 | 0.01486
 | = 20% | 0.1210 | 0.01623
 | = 35% | 0.1429 | 0.01521
 | = 100% | 0.7125 | 0.03817
N | Method | translation drift (m) | rotation drift (degree)
2000 |  | 0.1096 | 0.01486
 |  | 0.1210 | 0.01623
 |  | 0.1429 | 0.01521
 |  | 0.7125 | 0.03817
ICP results after moving out percent of samples out of non-ROI area