## Slide 1: Modified Y prediction
Y Prediction propagate MVs slower than 3DRS
  Modified Y structure only cover 2/4 quarters
    We need candidate structure have better coverage
T
T
Modified Y structure
T,
T
3DRS structure
T
T
First Iteration
Second Iteration
S U
S U
S U
S U
S U
S U
S U
S U

## Slide 2: 3DRS vs Y Prediction
3DRS has better convergence speed
  Can be noticeable the differences in the first frame
  Little differences when the result is converged
More important for sequences with global motion
  Faster convergence for background area
3DRS
Y prediction
Background area
Global motion
Small lobal motion

## Slide 3: New Candidate Structure
First iteration
  Use 3 candidates from top line
    Candidate from top line have better quality
    They are from current iteration
  Update candidates are generated for 2 best candidates
  Temporal candidate provide a lookahead to convergence direction
Second iteration
  The temporal candidate is move to current position
    To preserve result of large motion MVs
The new candidate structure have better coverage
S U
Z
T
First iteration
S
T
S
Second Iteration
Total candidates
T
S
T
S
S U
S U
S U
S U
S U
S U
S U

## Slide 4: Additional candidate structures
Others candidate structures used for comparison
Notation
  (1) 3DRS
  (2) Y prediction
  (3) Modified Y Prediction
  (4) Our structure
  (5) (6) Two structures as above respectively
T
S
T
S
S U
S U
S U
S U
S
S
4 candidates from top line More complexity than ours
T
S
T
S
S U
S U
S U
S U
S
S
5 candidates from top line More complexity than ours
S
S

## Slide 5: Structure comparison
Halo4_first frame (INIT)_First iteration
(1)
(2)
(3)
(4)
(5)
(6)

## Slide 6: Structure comparison
Halo4_first frame (INIT)_Second iteration
(1)
(2)
(3)
(4)
(5)
(6)

## Slide 7: Structure comparison
Halo4_second frame
(1)
(2)
(3)
(4)
(5)
(6)

## Slide 8: Structure comparison
Alley_1_first frame (INIT)_First iteration
(1)
(2)
(3)
(4)
(5)
(6)

## Slide 9: Structure comparison
Alley_1_first frame (INIT)_Second iteration
(1)
(2)
(3)
(4)
(5)
(6)

## Slide 10: Structure comparison
Chart: 
1st frame | 33.5373 | 32.5449 | 33.4571 | 32.2343 | 33.4103 | 33.5099
2nd frame | 33.7568 | 33.3732 | 33.731 | 32.815 | 33.8028 | 33.7434
average | 33.9883 | 33.7077 | 33.9775 | 33.6375 | 33.9762 | 33.9785
Halo4 PSNR
Halo4 SSIM
Alley_1 PSNR
Alley_2 PSNR
Chart: 
1st frame | 34.8134 | 34.3025 | 34.431 | 34.228 | 34.7254 | 34.7561
2nd frame | 34.781 | 34.6742 | 34.7413 | 34.7323 | 34.8234 | 34.8491
average | 34.4598 | 34.2876 | 34.4361 | 34.3212 | 34.5691 | 34.5216
Chart: 
1st frame | 38.2697 | 38.0482 | 38.2184 | 38.1861 | 38.2439 | 38.2916
2nd frame | 38.2944 | 38.1405 | 38.2661 | 38.1704 | 38.2 | 38.2339
average | 38.2806 | 38.1265 | 38.2417 | 38.1948 | 38.2168 | 38.2545
Chart: 
1st frame | 0.89502 | 0.83824 | 0.88734 | 0.81963 | 0.88664 | 0.89046
2nd frame | 0.90518 | 0.88807 | 0.90282 | 0.85549 | 0.90573 | 0.90397
Average | 0.90477 | 0.89235 | 0.90443 | 0.88645 | 0.90468 | 0.90498

## Slide 11: Structure comparison
Interpolation result
Conclusion
  Modified Y prediction (2) and (4) have worst results
  3DRS (1) have best and stable result
  Performance of our structure (3) and (5) (6) are close
 |  | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 | 
 |  | PSNR | SSIM | PSNR | SSIM | PSNR | SSIM | PSNR | SSIM | PSNR | SSIM | PSNR | SSIM
halo4 | 1st frame | 33.5373 | 0.89502 | 32.5449 | 0.83824 | 33.4571 | 0.88734 | 32.2343 | 0.81963 | 33.4103 | 0.88664 | 33.5099 | 0.89046
 | 2nd frame | 33.7568 | 0.90518 | 33.3732 | 0.88807 | 33.731 | 0.90282 | 32.815 | 0.85549 | 33.8028 | 0.90573 | 33.7434 | 0.90397
 | Average | 33.9883 | 0.90477 | 33.7077 | 0.89235 | 33.9775 | 0.90443 | 33.6375 | 0.88645 | 33.9762 | 0.90468 | 33.9785 | 0.90498
rimball | 1st frame | 37.1264 | 0.93798 | 36.9982 | 0.9363 | 37.0257 | 0.93745 | 37.0487 | 0.93704 | 37.0776 | 0.93772 | 37.0696 | 0.9373
 | 2nd frame | 40.6061 | 0.97342 | 40.7664 | 0.9735 | 40.7054 | 0.97343 | 40.6931 | 0.97302 | 40.6517 | 0.97317 | 40.7001 | 0.97338
 | Average | 38.8079 | 0.96041 | 38.8468 | 0.96047 | 38.8235 | 0.96089 | 38.8089 | 0.96041 | 38.8151 | 0.96046 | 38.8033 | 0.95979
alley_1 | 1st frame | 34.8134 | 0.89918 | 34.3025 | 0.87711 | 34.431 | 0.88491 | 34.228 | 0.87511 | 34.7254 | 0.89675 | 34.7561 | 0.89744
 | 2nd frame | 34.781 | 0.89882 | 34.6742 | 0.89316 | 34.7413 | 0.89735 | 34.7323 | 0.8948 | 34.8234 | 0.89912 | 34.8491 | 0.89919
 | Average | 34.4598 | 0.88809 | 34.2876 | 0.87843 | 34.4361 | 0.88628 | 34.3212 | 0.88105 | 34.5691 | 0.89096 | 34.5216 | 0.88874
alley_2 | 1st frame | 38.2697 | 0.95498 | 38.0482 | 0.95339 | 38.2184 | 0.95332 | 38.1861 | 0.95387 | 38.2439 | 0.95507 | 38.2916 | 0.95452
 | 2nd frame | 38.2944 | 0.95491 | 38.1405 | 0.95459 | 38.2661 | 0.95455 | 38.1704 | 0.95484 | 38.2 | 0.95459 | 38.2339 | 0.95487
 | Average | 38.2806 | 0.95248 | 38.1265 | 0.95151 | 38.2417 | 0.95168 | 38.1948 | 0.95167 | 38.2168 | 0.95148 | 38.2545 | 0.95234

## Slide 12: MAP vs 3DRS
Computation complexity
  MAP vs original 3DRS vs our version 3DRS
    MAP use 3 level
    Search range 16x8 at top level
  Number of candidate per each block
  MAP code also have many more algorithm
    Occlusion detection and handling
    Repetition pattern code
    ….
 |  | MAP | Our 3DRS | Original 3DRS
top level |  | 128 |  | 
2nd level |  | 36 |  | 
bottom level | normal block | 36 | 7 (first) + 6 (second) | 6 (first) + 6 (second)
 | large-motion block |  | 15 (first) + 6 (second) | 
Total |  | 53 | 13->21 | 12

## Slide 13: MAP vs 3DRS
Rimball
1st frame
2nd frame
1st frame
2nd frame
MAP
Our 3DRS
Original 3DRS (Y)

## Slide 14: MAP vs 3DRS
Balldrop
1st frame
2nd frame
1st frame
2nd frame
MAP
Our 3DRS
Original 3DRS (Y)

## Slide 15: MAP vs 3DRS
SoccerDrill3
Frame 48
Frame 50
Frame 48
Frame 50
MAP
Our 3DRS
Original 3DRS (Y)

## Slide 16: MAP vs 3DRS
MAP result is noisy in flat area
MAP
Our 3DRS
Original 3DRS (Y)
SmallObject_Golf_4
SoccerDrill3

## Slide 17: MAP vs 3DRS
Interpolation result
Chart: rimball
 | 32.457 | 29.0706 | 32.2825
Chart: balldrop
 | 30.4751 | 28.9913 | 31.1768
Chart: SoccerDrill1
 | 28.6272 | 26.7478 | 27.2096
Chart: SoccerDrill3
 | 27.7883 | 25.1461 | 26.6324
Average PSNR
1: MAP 2: Original 3DRS (Y) 3: Our 3DRS

## Slide 18: MAP vs 3DRS
Interpolation result
Conclusion
  Overall result: MAP > Our 3DRS > Original 3DRS (Y prediction)
    However, MAP could be noisy in flat area
  For large motion
    Original 3DRS could not handle large motion
 | MAP |  | Original 3DRS (Y prediction) |  | Our 3DRS | 
 | PSNR | SSIM | PSNR | SSIM | PSNR | SSIM
Rimball | 32.457 | 0.96393 | 29.0706 | 0.96498 | 32.2825 | 0.96385
balldrop | 30.4751 | 0.98477 | 28.9913 | 0.9842 | 31.1768 | 0.989
soccerdrill1 | 28.6272 | 0.95322 | 26.7478 | 0.95056 | 27.2096 | 0.9631
soccerdrill3 | 27.7883 | 0.96456 | 25.1461 | 0.9628 | 26.6324 | 0.96524